## Slide 1: Google Summer of Code Rigorous support of Vertical Datums within OGRSpatialReference
Gottfried Mandlburger and Johannes Otepka
gm@ipf.tuwien.ac.at, jo@ipf.tuwien.ac.at
with contributions from:
Nicolas David: nicolas.david@ign.fr
IGN - Institut National de l'Information Géographique et Forestière

## Slide 2: Spatial Referencing
OpenGIS® Implementation Specification: Coordinate Transformation Services
Available at: http://www.opengeospatial.org/standards/ct
Generic description of spatial reference systems
  Known Text (WKT) representation
  Horizontal systems (geographic and projected systems)
    Reference spheroids (SPHERIOD)
    Geodetic datum transformation (TOWGS84)
    Map projections (PROJECTION)
  Vertical systems
    Vertical datum (VERT_DATUM)
  Compound Systems (horizontal + vertical  3D)
Implementations available:
  GDAL/OGR library: Spatial reference classes (built upon PROJ4 library)
Existing problems
  No standards for vertical transformations available
  Different approaches for transition: national  global reference systems

## Slide 3: Coordinate Transformation: Trans-national  National via 7-P-Trafo
National sytem
Orthometric heights,
(AT: MGI)
Trans-national sytem, ellipsoidal heights, (EU: ETRS89)
x, y, H
Φ, λ, H
UTM33
GRS80
X, Y, Z
ETRS89
7-Parameter-Trafo
Geodetic Datum Transition via Spatial Similarity Transformation
X‘, Y‘, Z‘
x‘, y‘, h
Φ‘, λ‘, H‘
GK-M31
Bessel
MGI
Geoid
x, y Map coordinates
h, H Orthometric/ellipsoidal height
Φ, λ geographic coordinates
X, Y, Z geocentric coordinates
Homogeneous system
In-homogeneous historic system

## Slide 4: Coordinate Transformation: Trans-national  National via Grid Shifts
NTv2 (National Transformation v2) grid shifts
  Developed in Canada
  Adopted for USA, Australia, Germany (BeTA2007), Austria (GIS-Grid), ...
  Became quasi-standard
National sytem (AT: MGI)
Trans-national sytem (EU: ETRS89)
x, y, H
Φ, λ, H
UTM33
GRS80
x‘, y‘, h
Φ‘, λ‘, H‘
GK-M31
Bessel
Geoid
Grid shift Φ‘ = Φ + dΦ, λ‘ = λ + d λ
Drawbacks
  Not implemented as OGC Standard
  Merges datum transition and inhomogeneities of national grids
  Height information is lost
  National height anomalies are not compensated (2D only)

## Slide 5: OGC: Coordinate Transformation Services – Well Known Text Representation (example)
OpenGIS® Implementation Specification: Coordinate Transformation Services
  http://www.opengeospatial.org/standards/ct
Well-Known Text Representation of Spatial Reference Systems
PROJCS["OSGB 1936 / British National Grid",
GEOGCS["OSGB 1936",
DATUM["OSGB_1936",
SPHEROID["Airy 1830",6377563.396,299.3249646, AUTHORITY["EPSG","7001"]],
TOWGS84[375,-111,431,0,0,0,0],
AUTHORITY[["EPSG","6277"]],
PRIMEM["Greenwich",0,AUTHORITY["EPSG","8901"]],
UNIT["DMSH",0.0174532925199433,AUTHORITY["EPSG","9108"]],
AXIS["Lat",NORTH],
AXIS["Long",EAST],
AUTHORITY[["EPSG","4277"]],
PROJECTION["Transverse_Mercator"],
PARAMETER["latitude_of_origin",49],
PARAMETER["central_meridian",-2],
PARAMETER["scale_factor",0.999601272],
PARAMETER["false_easting",400000],
PARAMETER["false_northing",-100000],
UNIT["metre",1,AUTHORITY["EPSG","9001"]],
AXIS["E",EAST],
AXIS["N",NORTH],
AUTHORITY[["EPSG","27700"]],
Quelle: http://www.opengeospatial.org/standards/ct

## Slide 6: Height systems
Source: Briese et al., 2012: Transformation von GNSS-Höhen in österreichische
Gebrauchshöhen mittels einer Transformationsfläche (Höhen-Grid)

## Slide 7: Height systems
Physical nature of heights (gravity field of the Earth)
geoid = aequi-potential surface in mean sea level
Height differences = potential difference
Geo-potential cote:

## Slide 8: Height systems
Orthometric heights
Normal heights
Dynamic heights
Spherical heights
“Heights in use” (historically grown height systems, often in homogeneous)

## Slide 9: Inhomogenities of Austrian National Reference System (MGI)
0 1m 2m

## Slide 10: Austrian Federal Office of Metrology and Surveying (BEV) – Geoid model
Austrian Geoid 2008 – Reference Ellipsoid Bessel (MGI)
Accuracy: ± (2-3) cm
Undulations: -2,5 - 3,5 m
Quelle: http://www.bev.gv.at

## Slide 11: BEV - Height correction model
Modell NIV: aus Formel über Normalhöhe mit Verdichtung in die Fläche über Bougeranomalie
Vertical correction model compensating height anomalies in the Austrian national height system based on nivellement points
Transformation: „used heights (MGI)  orthometric heights (EVRS)
Source: http://www.bev.gv.at

## Slide 12: BEV GIS-GRID (=Ntv2 grid for Austria)
GRID (Raster) in geographic coordinate system ,  ; grid width z.B. 30“x45“ ( ≈ 1x1 km )
Each grid post contains correction values d, d
Derived from 28.120 control points (coordinates available in both MGI und ETRS89 system); Transformation accuracy < 15 cm
GIS - GRID
49°03’00“ 9°30’00“
46°21’00“ 17°09’45“
30 arcsec
45 arcsec
Source: http://www.bev.gv.at

## Slide 13: Issues
Transformation from ellipsoidal (geometric) to orthometric (physical) heights requires geoid model (quasi geoid for dynamic/normal heights)
In-homogeneity of historical height systems can be corrected with additional height correction models: hell  [geoid]  hortho [vertic. corr. model]  hused
Additional (optional) constant vertical offset (tidal diff., local heights, …)
Additional (optional) z-scaling
Geoid models are normally provided in geographic coordinates (GEOGCS; φ,λ). Thus, linkage between GEOGCS and VERT_CS would be necessary
Geoids are normally provided as rasters. Thus, (bi-linear) interpolation at arbitrary positions is required.
How to specify vertical CS (including geoids, height corr. models, height offsets) in OGC Coordinate Transformations (CT) Services spec.? This issue does not have to be tackled within the GSoC project
Height correction should be performed on the GEOGCS (φ,λ) level

## Slide 14: Implementation issues
Available libraries
  GDAL/OGR (Spatial Reference class)
  Proj4 (currently doing most of the transformation job)
  ... ...
Class interface:
  Based on OGR Spatial reference
  Add members/functions for vertical component
    SetGeoidModel( char* psz_geoidfile )
    SetHeightCorrModel( char* psz_geoidfile )
    SetHeightOffset( const double d_offset )
    .... ...
Allow vertical transformations for all systems based on GEOGCS

## Slide 15: Implementation issues
Support of different GEOID File Format
  Using OGR different raster formats could easily be supported
Library dependency
  PROJ.4 is an independent library
  OGR depends on PROJ.4
Technical solution for vertical transformation
  Inside PROJ.4 with GEOID interpolation calls to OGR
    + Current transformation workflow is preserved
    - PROJ.4 loses independence
  Full transformation workflow inside OGR (favored by IPF)
    + Transformation code at one place
    - double transformation code in PROJ.4 and OGR (rewrite pj_transform)
Optional additional Libraries
  The GeographicLib could be usefull (parts or full library). http://geographiclib.sourceforge.net/html/index.html

## Slide 16: Implementation issues
Current Transformation class (OGR)
  OGRProj4CT (derived from OGRCoordinateTransformation) wraps the transformation call to pj_transform
New Transformation Implemation
  A new class e.g. OGRProj4CT3D (also derived from OGRCoordinateTransformation) should be written. Containing the changed/improved pj_transform code

## Slide 17: Generic Transformation Path (status quo)
PROJ4 (pj_transform pseudo code):
  projected coordinate (proj)
  geographic coordinate
  scale /meridian offset transformation
  geoid transform
  geographic to wgs84 :
  -> grid shift
  -> geographic to geocentric -> 3/7 parameter transform
  wgs84 to geographic :
  -> grid shift
  -> geographic to geocentric -> three/seven parameter transform
  geoid transform
  scale /meridian offset transformation
  geographic coordinate (inverse proj)
  projected coordinate

## Slide 18: Generic Transformation Path (3D add-ons)
PROJ4 (pj_transform pseudo code):
  projected coordinate (proj)
  geographic coordinate
  scale /meridian offset transformation
  generic height transformation (geoid + height.corr. + z offset/scale)
  geographic to wgs84 :
  -> grid shift
  -> geographic to geocentric -> three/seven parameter transform
  wgs84 to geographic :
  -> grid shift
  -> geographic to geocentric -> three/seven parameter transform
  generic height transformation (geoid + height.corr. + z offset/scale)
  scale /meridian offset transformation
  geographic coordinate (inverse proj)
  projected coordinate

## Slide 19: Additional ideas
3D grid shift
  Current status: Ntv2 only 2D
  3D-extension desirable (not within GSoC project)
De-coupling in-homogeneities of national systems from datum transformation
  Status quo:
    geographic coo. (datum 1) 
    grid shift 
    geographic coo. (datum2)
  Desired (optional)
    geographic coo. (datum 1) 
    grid shift (national in-homogeneities only) 
    Homogenized geographic coo. (datum 1) 
    to wgs84
    Three/seven parameter transformation
    … … (back again)

## Slide 20: Proposed way of preceeding
Spatial Reference Systems:
Based on OGRSpatialReference class
Derived class OGRSpatialReference3D (working title)
Add members/functions for vertical transformation
  Geoid model
  Additional height correction model
  z offset and scale
Transformations:
Based on OGRCreateCoordinateTransformation
Derived class OGRCreateCoordinateTransformation3D
Make OGRCreateCoordinateTransformation ::transform function virtual
Re-write OGRCreateCoordinateTransformation3D::transform (cf. Slide: Generic Transformation Path (3D add-ons))